## Slide 1
MTT cell proliferation assay
3-(4,5-dimethylthiazol-2-yl)-2,5-diphenyltetrazolium bromide to its insoluble formazan

## Slide 2
Applications:
Cell proliferation assays
Cytotoxicity analysis
Apoptosis screening

## Slide 3
Equipment and Materials Required
Microtiter plate reader with 650- and 570-nm filters
Microtiter plate (flat-bottomed)
Inverted microscope
Sterile tubes (5 mL)
Multi-channel pipette
Serological pipettes
37°C incubator
Sterile pipette tips
Laminar flow hood

## Slide 4
Step Action
1 Harvest suspension cells by centrifugation. Adherent cells should be released from their substrate by trypsinization or scraping.
2 Resuspend cells at 1 x 106 per mL.
3 Prepare serial dilutions of cells in culture medium from 1 x 106 to 1 x 103 cells per mL.
4 Plate out, in triplicate, 100 μL of the dilutions into wells of a microtiter plate.
5 Include three control wells of medium alone to provide the blanks for absorbance readings
6 Incubate the cells under conditions appropriate for the cell line for 6 to 48 hours
(to recover from handling). The time required will vary but 12 hours to overnight
is sufficient for most cell types.
7- Add 10 μL of MTT Reagent to each well, including controls.
8- Return plate to cell culture incubator for 2 to 4 hours.

## Slide 5
9- Periodically view the cells under an inverted microscope for presence of intracellular
punctate purple precipitate.
10- When the purple precipitate is clearly visible under the microscope add 100 μL DMSO Dimethyl sulfoxide into each well to dissolve the formazan by pipetting up and down several times gently; do not shake, including controls.
11- Leave plate with cover in the dark for 2 to 4 hours or overnight at room temperature.
12- Remove plate cover and measure the absorbance in each well, including the
blanks, at 570 nm in a microtiter plate reader. [Absorbances can be read with any
filter in the wavelength range of 550 - 600 nm. The reference wavelength should
be higher than 650 nm. The blanks should give values close to zero (+/- 0.1).]
13- If the readings are low return the plate to the dark for longer incubation.
14- Determine the average values from triplicate readings and subtract the average
value for the blank. Plot absorbance against number of cells/mL. The number of
cells to use in your assay should lie within the linear portion of the plot and yield
an absorbance of 0.75 - 1.25.

## Slide 6
MTT assay
The MTT assay and the MTS assay are colorimetric assays for measuring the activity of enzymes that reduce MTT or close dyes (XTT, MTS, WSTs) to formazan dyes, giving a purple color
The main application allows to assess the viability (cell counting) and the proliferation of cells (cell culture assays)
It can also be used to determine cytotoxicity of potential medicinal agents and toxic materials, since those agents would stimulate or inhibit cell viability and growth

## Slide 7
• The MTT Cell Proliferation and Viability Assay is a safe, sensitive, in vitro assay for the measurement of cell proliferation or, when metabolic events lead to apoptosis or necrosis, reduction in cell viability.
• Cells are cultured in flat-bottomed, 96-well tissue culture plates. The cells are treated as per experimental design and incubation times are optimized for each cell type and system.
• The tetrazolium compound MTT (3-[4, 5-dimethylthiazol-2-yl]-2, 5-
diphenyltetrazolium bromide) is added to the wells and the cells are
incubated. MTT is reduced by metabolically active cells to insoluble purple formazan dye crystals by mitochondrial enzymes associated with metabolic activity. The reduction of MTT is primarily due to glycolytic activity within the cell and is dependent upon the presence of NADH and NADPH